## Slide 1
End-use Load Profiles for the U.S. Building Stock
Technical Advisory Group Meeting #10
April 22, 2021
Natalie Mims Frick, LBNL

## Slide 2: Logistics
We are recording the webinar and breakout groups.
Because of the large number of participants on the phone, please keep yourself muted during presentations.
Please use the chat box to send us clarifying questions during presentations. You can chat or unmute yourself to ask a question during our designated discussion time.
Links to the slides are in the chat box.

## Slide 3: Today’s agenda
 | Mountain Time
Welcome | 10:00 - 10:05
Data publication plan overview | 10:05 - 10:25
Commercial calibration update | 10:25 - 11:10
Breakout Room 1: Deep dive on commercial calibration Breakout Room 2: Electric vehicle infrastructure projection and charging load profile tool | 11:10 - 11:50
Plenary 3 - What’s next | 11:50 - 12:25
Wrap up | 12:25 -12:30

## Slide 4: Selecting your breakout room
Room 1: Deep dive on commercial calibration. In this breakout session we will answer questions that members have on our commercial calibration. We can discuss questions pertaining to plenary presentation, past calibration results or other aspects of our commercial calibration process.
Room 2: Electric vehicle infrastructure projection and charging load profile tool. NREL researcher Eric Wood will presention EVI-Pro Lite, which is a tool that provides a simple way to estimate how much electric vehicle charging a state or city might need and how the mix of vehicle types and charging infrastructure types affects the charging load profile.
Breakout rooms will be recorded.

## Slide 5: What’s next?
What additional resources or effort is of most interest to you or your organization?
What additional data or functionality would be most useful for our residential end use load shapes?
What additional data or functionality would be most useful for our commercial end use load shapes?
What additional model functionality would be useful?
What topics do you hope we will cover in our final two TAG meetings?

## Slide 6
EULP Data Publication
Andrew Parker
April 22, 2021

## Slide 7: Same Data, Multiple Scales
Aggregates
Individual Buildings
Web Viewer
Real data will be spikier

## Slide 8: Pre-aggregated Load Profiles
Aggregates
Individual Buildings
Web Viewer
Pre-aggregated EULPs by building type for:
U.S. States (contiguous)
ASHRAE Climate Zones
DOE Building America Climate Zones
Electric System ISOs
U.S. Census Public Use Microdata Area*
U.S. Counties
*PUMA is an area with ~200k people; ~2,400 in U.S.
Format:
CSV files (for Excel, etc. ease of use)
Additional Data:
Count of models included per aggregation
List of model IDs per aggregation
Model characteristics by ID
Timeseries mean, stdev, and range

## Slide 9: VizStock Web Interface
Aggregates
Individual Buildings
Web Viewer
View End Use Load Profiles
View distributions of building characteristics
Filter by building characteristic
Filter by geography
Select time window
Download CSV of results

## Slide 10: Individual Buildings – Load Profiles & Models
Aggregates
Individual Buildings
Web Viewer
Individual Building End Use Load Profiles
~450,000 residential
~350,000 commercial
Full dataset will be 10’s of terabytes
Plan to include high-level instructions for loading this dataset using one cloud-based big-data analysis tool
Format:
Folders with a series of Apache parquet* files
  Likely 1 file per building, with IDs in names
In Amazon S3 bucket or similar
Additional Data:
Model characteristics by ID
Model in OpenStudio (.osm) format
*https://parquet.apache.org/

## Slide 11: 2 Sets of Weather Data = 2 Sets of EULPs
Typical Meteorological Year (TMY3)
Widely accepted/expected by utilities, regulators, etc.
Weather is not coordinated across regions
Actual Meteorological Year (AMY)
Using 2018 NOAA data
 | Weather Data from Year | 
Month | Denver, CO | Boulder, CO
January | 1995 | 1987
February | 1994 | 1990
March | 1991 | 1981
April | 1999 | 1986
Format:
CSV timeseries data for each location used
  Dry bulb temperature
  Relative humidity
  Solar direct normal irradiation
  Solar diffuse horizontal irradiation
  Wind speed
  Building characteristics
Location used for each Model
2 locations 40 miles apart use data from different years for the same month

## Slide 12: Time Stamps & Time Zones
Time Zones:
Data will be provided in UTC
Time Stamps:
Wrap data from first few hours of year back to the end
Creates a single, aligned 1 year worth of data

## Slide 13
Questions & Discussion

## Slide 14: Residential Building Types & End Uses
Residential Building Types | Residential End Uses
Single-Family Detached | Heating
Single-Family Attached | Cooling
Multifamily 2–4 Units | Furnace/AC fan
Multifamily 5+ Units (1-3 stories) | Boiler pumps
Multifamily 5+ Units (4-7 stories) | Vent. fans
Multifamily 5+ Units (8+ stories) | Water heating
 | Interior Lights
 | Exterior Lights
 | Misc. plug loads
 | Refrigerator
 | Clothes washer
 | Clothes dryer
 | Dishwasher
 | Cooking Range

## Slide 15: Commercial Building Types & End Uses
Commercial Building Types | Commercial End Uses
Small Office | Heating
Medium Office | Cooling
Large Office | Interior Lighting
Stand-alone Retail | Exterior Lighting
Strip Mall | Interior Equipment
Primary School | Exterior Equipment
Secondary School | Fans
Outpatient Healthcare | Pumps
Hospital | Heat Rejection
Small Hotel | Humidification
Large Hotel | Heat Recovery
Warehouse (non-refrigerated) | Water Systems
Quick Service Restaurant | Refrigeration
Full Service Restaurant | 

## Slide 16: Residential Building Characteristics
Residential Model Characteristics | (continued) | (continued)
ahs_region | heating_fuel | location_latitude
applicable | heating_setpoint | location_longitude
ashrae_iecc_climate_zone_2004 | heating_setpoint_has_offset | location_region
bathroom_spot_vent_hour | heating_setpoint_offset_magnitude | location_state
bedrooms | heating_setpoint_offset_period | mechanical_ventilation
building_america_climate_zone | holiday_lighting | misc_extra_refrigerator
ceiling_fan | hot_water_distribution | misc_freezer
census_division | hot_water_fixtures | misc_gas_fireplace
census_region | hvac_system_cooling | misc_gas_grill
climate_zone_ba | hvac_system_cooling_type | misc_gas_lighting
climate_zone_iecc | hvac_system_heat_pump | misc_hot_tub_spa
clothes_dryer | hvac_system_heating_electricity | misc_pool
clothes_washer | hvac_system_heating_fuel_oil | misc_pool_heater
clothes_washer_presence | hvac_system_heating_natural_gas | misc_pool_pump
cooking_range | hvac_system_heating_none | misc_pool_schedule
cooking_range_schedule | hvac_system_heating_other_fuel | misc_well_pump
cooling_setpoint | hvac_system_heating_propane | natural_ventilation
cooling_setpoint_has_offset | hvac_system_is_heat_pump | neighbors
cooling_setpoint_offset_magnitude | hvac_system_is_shared | occupants
cooling_setpoint_offset_period | hvac_system_shared_electricity | orientation
corridor | hvac_system_shared_fuel_oil | overhangs
county | hvac_system_shared_natural_gas | plug_loads
days_shifted | hvac_system_shared_none | plug_loads_schedule
dehumidifier | hvac_system_shared_other_fuel | puma
dishwasher | hvac_system_shared_propane | pv
door_area | infiltration | radiant_barrier
doors | insulation_crawlspace | range_spot_vent_hour
ducts | insulation_finished_basement | refrigeration_schedule
eaves | insulation_finished_roof | refrigerator
electric_vehicle | insulation_interzonal_floor | roof_material_finished_roof
geometry_building_number_units_hl | insulation_pier_beam | roof_material_unfinished_attic
geometry_building_number_units_mf | insulation_slab | sample_weight
geometry_building_number_units_sfa | insulation_unfinished_attic | solar_hot_water
geometry_building_type_acs | insulation_unfinished_basement | state
geometry_building_type_recs | insulation_wall | units_modeled
geometry_floor_area | interior_shading | units_represented
geometry_floor_area_bin | iso_rto_region | usage_level
geometry_foundation_type | lighting | vintage
geometry_garage | lighting_interior_use | vintage_acs
geometry_perimeter_footprint_ratio | lighting_other_use | water_heater
geometry_stories | location | window_areas
geometry_wall_type | location_city | windows

## Slide 17: Commercial Building Characteristics
Commercial Model Characteristics | (continued)
building_type | cooling_source_fuel
climate_zone | heating_source_fuel
weather_file_name | hvac_delivery_type
rentable_area | service_water_heating_source_fuel
number_stories | kitchen_makeup
aspect_ratio | exterior_lighting_zone
total_bldg_floor_area | onsite_parking_fraction
bottom_story_ground_exposed_floor | energy_code_when_built
building_height_relative_to_neighbors | energy_code_when_envelope_last_updated
building_rotation | energy_code_when_exterior_lighting_last_updated
floor_to_floor_height | energy_code_when_hvac_last_updated
party_wall_stories_west | party_wall_fraction
single_floor_area | party_wall_stories_east
story_multiplier | party_wall_stories_north
top_story_exterior_exposed_roof | party_wall_stories_south
window_to_wall_ratio | energy_code_when_interior_equipment_last_updated
hvac_system_type | energy_code_when_interior_lighting_last_updated
energy_code_when_service_water_heating_last_updated | 
weekday_operation_start_time | 
weekday_operation_duration | 
weekend_operation_start_time | 
weekend_operation_duration | 

## Slide 18
Commercial Calibration Update
Region 2 & Overall Status
Andrew Parker
Matthew Dahlhausen
April 22, 2021

## Slide 19: Commercial Calibration Team
Andrew
Parker
Chris
CaraDonna
Dr. Janghyun Kim
Elaina
Present
Dr. Matthew
Dahlhausen
Amy
LeBar
Dr. Rajendra
Adhikari
Dr. Lixi
Liu
Dr. Anthony
Fontanini

## Slide 20: Calibration Progress
About 60% through the commercial calibration timeline
Finished Region 1 of 4 (Ft. Collins) in Fall 2020
  Paused commercial calibration while awaiting AMI data
Finished Region 2 of 4 (Seattle, Portland) in February 2021 - today’s focus
Halfway through Region 3 of 4 (Cold/Very Cold) today
Region 4 of 4 (Southeast) June-August 2021
Notes: Commercial calibration is behind residential – started 3mo later, had delay due to AMI data availability

## Slide 21: Commercial AMI Data Challenges
Misclassification of buildings (outlier removal technique, see previous TAG presentation)
Partially-occupied buildings (outlier removal)
Knowingly/unknowingly missing large fraction of meters for a building (outlier removal)
Missing some timesteps for some meters (new method, described in later slides)
Knowingly missing a small fraction of the meters for a building
  Reason may vary between utilities (meters not all AMI, meters defunct, oversight)
  Current crude correction: assume equal area served by all meters, scale floor area
  Investigating prevalence of this situation and impact of this correction now
Unknowingly missing a small fraction of the meters for a building
  EUI likely within 3x median, load shape still reasonable… undetectable error?
For utilities, fundamental unit of reporting one meter, not buildings or sqft
Notes: We previously presented the challenges of identifying misclassified buildings
short version: removing very low outliers then applying 1/3-3X median band gets worst offenders
Found a new issue with Region 2 AMI data – missing longer periods from individual meters across the stock – explained later
We now have AMI data for 8 utilities in-hand and have starting comparing across and investigating them
New issue for some AMI datasets – utility said that 6 meters matched the building address, but only gave us data for 3
And possible issue for all datasets: due to address mismatches or other unknown features, we think we have all meters for a building, but unknowingly don’t
This is the most insidious type of error
Fortunately, because the EUI is inside of the 3x median filter, ability to greatly shift magnitude of AMI is limited
Currently investigating this

## Slide 22: Commercial AMI Confidence
Current Situation (all graphs in this slide deck)
Graphs show mean AMI (kWh/sqft per hr)
Dashed lines show mean +/- 10%
Overstates confidence in the mean of the AMI
Plan to Address:
Adjust AMI confidence bands based on sample size
  Realistic depiction of confidence in AMI mean
  Ranges likely large for building types and datasets with smaller sample sizes. Sometimes too large to inform model changes?
(Maybe) Focus on AMI for load shape comparison, use CBECS for load magnitude comparison
  Upside: don’t drive model changes with uncertain data
  Downside: CBECS data from different year, less geographically condensed
Other? – discuss during breakout
Notes: When comparing means of different EUIs by building type across all 8 utilities, shape differences make sense (higher summer peaks in FL than WA) but magnitudes don’t
Then, had the realization that we haven’t been appropriately mentally accounting for the sample size differences between utilities
When you start including confidence intervals, the apparent differences start to look less inexplicable
We believe we need to incorporate these confidence intervals into both our thinking and our presentations

## Slide 23: Commercial Calibration Dimensions
Com. Calibration
EIA 861m electricity, natural gas
EIA CBECS
Utility load research data (LRD)
Region 1 AMI data
Region 2 AMI data
Region 3 AMI data
Region 4 AMI data
Submeter end-uses
Annual gas and electricity EUIs by building type
Sub-metered end-use load data (10 datasets)
AMI data from Fort Collins municipal service territory (CO)
AMI data from (likely)
Horry County, SC;
Chatanooga TN;
Tallahassee, FL
Load duration curves and seasonal load shapes of ~16 utilities around U.S.
Annual and monthly electricity and natural gas consumption by state, sector
AMI data (aggregated by building type) from Seattle City Light, WA and Portland General Electric, OR
AMI data from Vermont; Maine; Cherryland, MI
Notes: We have been using submeter data to improve model inputs – presented today and in past
We have to date been relying almost exclusively on comparison to AMI data
We need to expand our horizons to other data sources (CBECS, EIA, and Load Research Data)
This was always part of the plan, but importance has increased due to newly-understood range in AMI
We are working on these comparisons right now but don’t have them ready to present

## Slide 24
Addressing Gaps in AMI Data

## Slide 25: Seattle AMI Challenges
Warehouse (n=300)
Seattle has two separate AMI recording systems
  One for smaller customers rolled out in 2018
  One for larger customers rolled out earlier
Many building types only have data from larger customers for some periods
They were working out kinks in smaller customer AMI rollout; only larger customers reading
More short outages in smaller customer AMI system; remaining data from large customers only

## Slide 26: Seattle AMI Challenges
As expected, fewer buildings means less energy for those timesteps
Warehouse (n=300)

## Slide 27: Seattle AMI Challenges
The meters that remain on are in the larger-customer AMI system.
This skews the EUI toward those buildings (higher) during meter outages
Warehouse (n=300)

## Slide 28: Seattle AMI Solution
Warehouse (n=300)
For calibration, drop data from timesteps where
# buildings < 30%

## Slide 29: Seattle AMI Solution (Implemented)
For calibration, drop data from timesteps where # buildings < 30%
Not all building type have same outage periods
Not all building types show as noticeable EUI bias during outage periods
In practice, filters are narrow and cover the outage periods exactly
Warehouse (n=300)
Notes: This filtering was done for the ami data comparison for Seattle

## Slide 30
Calibration Strategy

## Slide 31: Model Architecture
Building stock characteristics database
National
Climate/Region
State
County
Physics-based
computer modeling
Modeling Algorithms
Component Properties
Performance Curves
Schedules
Human Behavior
Weather
Data

## Slide 32: Calibration Process for One Region
Chart: 
| Region 1 Calibration | Region 2 Calibration | Region 3 Calibration | Region 4 Calibration | Region 5 Calibration
Region 1 | 0.28 | 0 | 0 | 0 | 0
Error
Focus on reducing error for one region at a time
Before
Calibration
After
Calibration
Keep an eye on impacts to other regions
Notes: The error in the first region at the end of region 1 calibration is NOT the final error we expect at the end of the project

## Slide 33: Calibration Process Over Time
Chart: 
| Region 1 Calibration | Region 2 Calibration | Region 3 Calibration | Region 4 Calibration | Region 5 Calibration
Region 1 | 0.28 | 0.21 | 0 | 0 | 0
Region 2 | 0.28 | 0.21 | 0 | 0 | 0
Error
Focus on reducing error for one region at a time
Keep an eye on impacts to earlier regions
Notes: At the end of each regional calibration:
Re-calculate Load Research Data comparison (18 utilities nationwide)
Re-calculate error for previously-calibrated regions

## Slide 34: Calibration Process Over Time
Chart: 
| Region 1 Calibration | Region 2 Calibration | Region 3 Calibration | Region 4 Calibration | Region 5 Calibration
Region 1 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 2 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 3 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 4 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 5 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Error
Calibration efforts for earlier regions
create better starting point for later regions
Notes: Because many building characteristics, modeling approaches, etc. are used by all regions, we expect that calibration efforts for Region 1 will lower the starting error for Region 2 lower.

## Slide 35: Calibration Process Over Time
Chart: 
| Region 1 Calibration | Region 2 Calibration | Region 3 Calibration | Region 4 Calibration | Region 5 Calibration
Region 1 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 2 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 3 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 4 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Region 5 | 0.28 | 0.21 | 0.14 | 0.105 | 0.07
Error
Improvements from later regions will improve results for regions focused on earlier
Notes: Re-emphasize: the error in the Region 1 at the end of Region 1 calibration is NOT the final error we expect at the end of the project; many of the improvements we make over time will cascade back and improve the error for previously calibrated regions.

## Slide 36: Summary of Commercial AMI Calibration Regions
Region 4
Region 5 (planned)
2
2
1
LADWP
(completed under previous project)
Fort Collins Utilities, CO
Seattle City Light
Portland General Electric
Portland, Maine (Efficiency Maine)
Vermont
(VEIC)
3
Cherryland, MI
3
Background colors are DOE Building America Climate Regions
3
4
Tallahassee, FL
EPB Chattanooga, TN
4
4
Horry County, SC

## Slide 37: Region 2 Focus: Major Schedules
Building stock characteristics database
National
Climate/Region
State
Physics-based
computer modeling
Modeling Algorithms
Weather
Data
Component Properties
Performance Curves
Schedules
Human Behavior
Lighting schedules
Plug load schedules
Operation schedules
County
HVAC Operation
Exterior Lighting
Notes: These will be relevant across all regions

## Slide 38: Region 2a – Seattle, WA
Seattle, WA (pop. ~745k) plus parts of adjacent suburbs
Municipal utility
AMI data from 2019 (aggregated by building type)
building_type | count
full_service_restaurant | 167
hospital | 12
large_hotel | 39
large_office | 137
medium_office | 109
outpatient | 162
primary_school | 43
quick_service_restaurant | 40
retail | 485
small_hotel | 25
small_office | 693
strip_mall | 941
warehouse | 633

## Slide 39: Region 2a – Seattle, WA – No Summer
Assign “season” to each month to enable comparison across regions
  Based on average daily temperatures in each month for weather used
    Winter/heating < 55°
    > 55° Shoulder < 70°F
    Summer/cooling > 70°F
  May not match what residents think of as seasons
  Therefore, “Summer” is missing in the Seattle graphs
Monthly Season Definitions

## Slide 40: Region 2b – Portland, OR
Portland (Portland General Electric)
Publicly-traded Utility
AMI data from 2019
building_type | count
full_service_restaurant | 391
hospital | 13
large_hotel | 92
medium_office | 13
outpatient | 530
primary_school | 105
quick_service_restaurant | 119
retail | 1,193
small_hotel | 59
small_office | 303
strip_mall | 1,215
warehouse | 2,511
Notes: Medium size city, partially urban, partially rural
Not huge building counts for all building types…EUIs hard to judge for things like hotels, large offices

## Slide 41: List of updates
Misclassification/Outlier Detection
Comparison of approaches w/ large Xcel dataset (presented in detail at TAG meeting)
New validation comparisons
AMI data from Seattle City Light (aggregated by building type)
AMI data from Portland General Electric
New capabilities
None
Baseload updates
Interior lighting schedule magnitude variability
Plug load schedule magnitude variability
Exterior lighting power density
Warehouse operation schedules (lighting, plug load, occupancy)
HVAC updates
Off cycle controls for packaged single-zone systems

## Slide 42
Baseload Updates
Notes: Going to go through the individual updates fairly quickly due to time,

## Slide 43: Update: Variability in Lighting & Plug-load Schedules
Task | Affected Building Type | Considerations
Interior lighting schedule magnitude variability | retail, food service, school, office | Magnitude variability (base-to-peak ratio) in schedules are captured from end-use (lighting & plug load) data. Standardized workflow added in ComStock to incorporate variability captured from end-use data. Lighting/Plug-load schedule variability improved.
Plug load schedule magnitude variability |  | 
Notes: Show what we did

## Slide 44: Base-to-Peak Ratio
Load (kW)
Time (1 day)
00:00
24:00
12:00
Base Load
Annual Peak Load
Base-to-Peak Ratio (BPR) = Base Load / Annual Peak Load
A way to describe to what degree loads are reduced at night
Notes: Show what we did

## Slide 45: Base-to-Peak Ratio
Load (kW)
Time (1 day)
00:00
24:00
12:00
Base-to-Peak Ratio (BPR) = Base Load / Peak Load
A way to describe to what degree loads are reduced at night
Modify BPR of existing schedules by changing the base load.
Original Schedule
Modified Schedule
Notes: Show what we did

## Slide 46: Update: Lighting & Plug-load Base-to-Peak Variability
Example measure results
Creating base-to-peak ratio (BPR) distributions
Lighting and plug load schedules were pulled from two commercial end use datasets that we procured.
A data clustering analysis was performed to group the schedules based on various BPR distributions resulting in 6 different cluster types covering all considered building types.
Distributions were calculated based on these clusters and implemented in the ComStock sampling approach as wkdy_bpr and wknd_bpr values.
Measure implementation
The measure sets the base period of interior lighting and equipment (plug load) schedules within a model to a BPR.
Two arguments: wkdy_bpr modifies weekday schedules, and wknd_bpr modifies weekend schedules.
Plug load electricity
Lighting electricity
Modify BPR: turn off less load at night
Modify BPR: turn off more load at night

## Slide 47: Impact: Lighting Base-to-Peak Variability
Before
After
Higher base load
Region 1 – Ft. Collins
Retail

## Slide 48: Impact: Plug Load Base-to-Peak Variability
No noticeable difference in plug load energy use; mostly adds diversity to stock
Before
After
Region 1 – Ft. Collins
Small Office
Notes: There is a slight difference (look at AM base load), but very little change

## Slide 49: Update: Exterior Lighting Power Density
Task | Affected Building Type | Considerations
Exterior lighting power density | buildings where exterior lighting is defined | Lighting power density in two sub-categories (parking and entry canopy) of exterior lighting are updated. Based on 2015 U.S. Lighting Market Characterization report.
Notes: Show what we did

## Slide 50: Update: Exterior Lighting Power Density
Various information from 2015 U.S. Lighting Market Characterization (LMC) report For parking applications (about 50% of total exterior lighting nationally)
Total # of Parking Lamps
83,519,000 systems
Avg Parking Light System Power
216 W/system
Avg Parking Lit Hours
16 hrs/day
Avg # of spots
13 lot-spots/system
2.5 garage-spots/system
Total lot/garage spots
610,000,000 lot-spots/nationwide
85,000,000 garage-spots/nationwide
Thornton, B. A., Wang, W., Lane, M. D., Rosenberg, M. I., & Liu, B. (2009). Technical support document: 50% energy savings design technology packages for medium office buildings (No. PNNL-19004). Pacific Northwest National Lab.(PNNL), Richland, WA (United States).
Possible to derive,
216 W/system 13 lot-spots/system = 16.615 W/lots-spots
16.615 W/lots-spots 405 sqft/lot-spots = 0.041 W/sqft (national average for parking lots only)
Notes: there are various info available in 2015 LMC (as shown in those boxes)
for understanding nationwide parking exterior light characteristics
and also can derive LPD with simple math by combining with info from PNNL study

## Slide 51: Update: Exterior Lighting Power Density
LMC’s weighted
average
= 0.041 W/ft2
ComStock (ASHRAE Standard) generally has much higher LPD definitions compared to LMC report. LPD definitions updated for each template based on weighted average.
Standard | 90.1 – 2004 | 90.1 – 2007 | 90.1 – 2010 | 90.1 – 2013 | DOE Ref 1980-2004
# of Buildings | 85652 | 96278 | 98128 | 28707 | 41235
Portion | 24% | 28% | 28% | 8% | 12%
Original LPD (W/ft2) | 0.15 | 0.15 | 0.1 | 0.1 | 0.18
Revised LPD (W/ft2) | 0.045 | 0.045 | 0.030 | 0.030 | 0.055
Notes: value derived in previous slide was used to create a new set of LPDs for each template
original ComStock values generally has higher LPD
and the new set of LPDs based on LMC was applied with values in red box.

## Slide 52: Update: Exterior Lighting Power Density
Before
After
Exterior lighting power reduction
Region 1 – Ft. Collins
Total – All Building Types
Notes: total load end use break down shows reduction in exterior lighting power consumption.

## Slide 53: Update: Warehouse Operation Schedules
Task | Affected Building Type | Considerations
Warehouse schedules (lighting, plug load, occupancy) | warehouse | Operations of warehouses were reviewed and reconsidered in terms of day types between weekdays and weekends.
Notes: - relaxing lunch load reduction not implemented yet. but soon to be updated.

## Slide 54: Update: Warehouse Operation Schedules
Based on end-use data (shown below) and AMI data (Fort Collins, Seattle, Portland), weekend warehouse operation assumptions in models disagreed with findings from utility data.
Warehouses in end-use data |  | 
Census Division | US State | Counts
EastNorthCentral | IL | 2
MidAtlantic | PA | 3
Mountain | CO | 2
Pacific | CA | 11
 | OR | 1
SouthAtlantic | MD | 1
WestSouthCentral | LA | 3
 | TX | 2
MON
TUE
WED
THU
FRI
SAT
SUN
No operations during weekends

## Slide 55: Update: Warehouse Operation Schedules
Before
After
Region 2b - Portland
Region 2b - Portland
Overshot warehouse schedule correction; some still have weekend operation

## Slide 56
HVAC Updates

## Slide 57: Update: HVAC Controls
Task | Affected Building Type | Methods
Updated fan cycling controls for PSZ systems | All buildings with PSZ systems | Before, systems were always on following HVAC operating hours, now fan are adjusted to provide ventilation only when occupied
DCV bug fix | Buildings with VAV systems that use 90.1-2010 or 2013 | DCV controls were not enabled and are now enabled per 90.1 standards
Minimal changes to loads because of limited applicability of control changes
Notes: Several building types are not included in this implementation due to insufficient data.

## Slide 58
Lighting Power Density Analysis

## Slide 59: Lighting Power Density Comparison
Lighting constitutes the majority of energy use
Lighting technologies have changed much faster than the rest of commercial building technologies
ComStock uses a technology rollover model, but only has standards up to 90.1-2013
“...the major change over time involved a significant transition to LED lighting power, which only represented 20 MW in 2014 (1% of regional commercial indoor lighting power). By 2019, that value had increased by more than 20 times to 419 MW, or 16% of the regional total.”
Source: NEEA Commercial Building Stock Assessment (CBSA) 2019

## Slide 60: Lighting Power Density – To Be Implemented
CBSA shows a 0.24 W/ft2 decrease (0.99  0.74 W/ft2) between 2014 and 2019
ComStock values, in 2019, show a <0.1 W/ft2 decrease between 2016 and 2019
ComStock LPDs are substantially higher than CBSA in key building types (warehouse, retail)
Will address by adding 90.1-2016, 90.1-2019 and a more aggressive rollover model
Source: NEEA Commercial Building Stock Assessment 2019

## Slide 61
Total Commercial Stock Status

## Slide 62: Region 1 – Fort Collins
Overestimating in all seasons, but potentially not all for the same reason
Notes: One thing to point out is at least this is filtered down to the building types we are modeling. Other data sources (EIA, LRD) will include all commercial sector.

## Slide 63: Region 1 – Fort Collins
Need to review shape to understand main drivers

## Slide 64: Region 1 – Fort Collins
Maybe overestimating fan energy?

## Slide 65: Region 2a – Seattle – Correction Since 2/28
Before correction
After correction
Suspicions about AMI EUIs led to additional investigation of building type mapping
Seattle was able to identify issue and correct mapping
AMI aggregations make more sense alone and compared to PGE
Before

## Slide 66: Region 2a - Seattle
Suspect much of this error due to aggressive lighting technology changes in pacific northwest in last 10 years

## Slide 67: Region 2a - Seattle

## Slide 68: Region 2a - Seattle
Suspect much of this error due to aggressive lighting technology changes in pacific northwest in last 10 years

## Slide 69: Region 2b - Portland
Same as Seattle; likely overestimating lighting power density

## Slide 70: Region 2b - Portland
Likely overestimating lighting power density

## Slide 71: Region 2b - Portland

## Slide 72
Building Type Focus

## Slide 73: Dominant Building Types by Area
Seattle
Warehouse, Strip Mall & Retail dominate building area for all 3 datasets
Fort Collins
Portland

## Slide 74
Warehouse

## Slide 75: Warehouse – 1 Fort Collins
Back to work! Need to minimize lunch break plug load dip
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 76: Warehouse – 2A Seattle
Lighting reduction will help, but not completely.
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 77: Warehouse – 2B Portland
Lighting power density reduction should help significantly
Overshot warehouse schedule correction; some still have weekend operation
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 78
Strip Mall

## Slide 79: Strip Mall – 1 Fort Collins
Seems like we’re getting weekend operating hours correct, but we’re overstating what is happening during those hours, especially Sundays.
Overshooting by quite a bit (more so than other seasons and retail winter). More pronounced “dog ears.” Similar thing happening on weekends as in summer.
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 80: Strip Mall – 1 Fort Collins
Overshooting, but shape looks good. Still missing some baseload. Check lighting?
Exterior lighting still looks like it’s coming on too early in the evening.
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 81: Strip Mall – 2A Seattle
Lighting reduction will help, but not completely. Need to look at HVAC operation as well.
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 82: Strip Mall – 2A Seattle
Lighting reduction will help, but not completely. Need to look at HVAC operation as well.
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 83: Strip Mall – 2B Portland
Lighting reduction will help, but not completely
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 84: Strip Mall – 2B Portland
Lighting reduction should help, but not entirely.
Need to investigate fan and HVAC operation schedules
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 85
Retail

## Slide 86: Retail – 1 Fort Collins
Overestimating on weekends (may be lighting issue). Our models have more weekend usage. Distribution of weekend operating schedules may need updating.
Nighttime setbacks could be causing the issue with low baseload. In the daytime, ComStock is still showing the bimodal peaks. This seems to be caused by the lighting schedules.
Odd nighttime trend with heating and fans. Could be cycling or truck unloads?
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 87: Retail – 1 Fort Collins
ComStock closer to AMI on peak days with higher load
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 88: Retail – 2a Seattle
Lighting update should make significant improvement
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 89: Retail – 2a Seattle
No Seattle AMI for Retail during this week b/c of meter outages
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 90: Retail – 2B Portland
Overshooting all days and missing some baseload. Model weekends show afternoon bump, that we don’t see in Region 1 models or AMI data.
Seeing flat shape on most days, which AMI data does not support. We are especially overestimating on the weekends. Might be missing cooling end use?
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 91: Retail – 2B Portland
Overshooting and baseloads are too low. Weekend operating hours seem too long (esp. in evening).
Seems like lighting is the culprit. May need more buildings that shutoff earlier
May be missing cooling from shoulder. Not enough base load, overshooting in middle of the day. Hours of operation are too square, check sch. distribution.
Notes: while samples for calibration are retained well for fort collins and PGE, seattle AMI data has time series data quality issue that makes the calibration comparison difficult for warehouse

## Slide 92
Tracking Quantities of Interest

## Slide 93: All Regions: Annual Error
Percent difference
Region 1
Region 2b
Region 2a

## Slide 94: Region 1 Focus: Total Error Metrics
Percent difference
Top 10 Days
Average of All Days
Peak Timing
Minutes difference
Overshooting winter & shoulder peaks

## Slide 95: Region 2a Focus: Total Error Metrics
Percent difference
Top 10 Days
Average of All Days
Peak Timing
Minutes difference
Overshooting peaks
Base load close
Peak shifted

## Slide 96: Region 2b Focus: Total Error Metrics
Percent difference
Top 10 Days
Average of All Days
Peak Timing
Minutes difference
Overshooting everything
Timing of winter peaks

## Slide 97
Areas for Improvement

## Slide 98: Next Steps: Model Improvements
Adjust space type ratios to create building subtypes (e.g., different kinds of warehouse buildings)
Adjust lighting power density by updating energy code adoption and technology rollover by state/year
Review distributions of schedule start & duration by building types
Review datasets of HVAC nighttime operation, especially RTUs
Continue emphasis on building types with biggest area/energy

## Slide 99: Conclusions
Spent much time and effort of misclassification/outliers
  Used monthly Xcel Energy data from 500,000 meters spanning 8 states (presented in detail at TAG meeting)
  Was necessary to get improve ground-truth data for calibration
Ran 4 iterations of ComStock incorporating 4 discrete changes (2 before getting Region 2 data)
  Saw general improvements in QOI metrics​, but still overpredicting in Region 2
  Most of the improvements made will carry over to the entire U.S.​
New/Updated visualizations
  AMI data from Seattle City Light (aggregated by building type)
  AMI data from Portland General Electric
Priority areas for improvement for next region
  Adjust lighting power density by updating energy code adoption and tech. rollover
  Review distributions of schedule start & duration by building types
Moving on to Region 3 (Vermont, Maine, and Cherryland, MI), but will continue tracking Region 1, 2a, 2b metrics
Notes: For Com, the truth data continues to prove to be the biggest priority

## Slide 100
Questions for Breakout

## Slide 101: First Impressions?
Given what we just showed, what are your gut reactions/impressions?
Will start at 11:15 Mountain Time

## Slide 102: Seed Questions
Are we missing something obvious in thinking about the confidence in the AMI data?
  What confidence interval to use? HEMS/CEMS samples targeted 80% CI I believe.
Given the confidence ranges, does the idea to 0-1 normalize mean shapes make sense?
  Obviously need to pair this with comparison of EUI distributions to CBECS
ComStock is modeling ~70-80% of the commercial stock
  EIA data represents 100% of commercial sector
  Issues with commercial vs. industrial classification in reporting by utilities, per EIA team
Given these limitations on the quality of the truth data, do you recommend any changes to our approach to reporting, prioritizing, etc.?
If you had to choose, would you focus more on getting individual end-use shapes correct than on matching utility overall load shapes?
If you had to choose, would you focus more on buildings that represent most of the stock (retail, strip mall, warehouse) or spread focus more evenly across types?

## Slide 103: EVI-Pro Lite: A Simplified Version of the Electric Vehicle Infrastructure Projection Tool

## Slide 104: The EV Infrastructure Projection Tool
NREL | 2
Simulation model to:
Estimate charging demand from EVs
Design supply of infrastructure
Informed by real-world data and integrated with models of vehicle adoption, mobility, station economics, and the grid
Originally developed through collaboration with the California Energy Commission and since applied at the city-, state-, and national-level
Spatial distribution of demand in San Francisco
CA Statewide Charging Load

## Slide 105
Travel Surveys
GPS Data
Direct Enumeration
Discrete Choice Models
PEV Efficiency (RouteE)
PEV Fleet Size &
PEV Attributes
EV-FAST + URDB
ADOPT, MA3T
EVI-Pro
Installation
Constraints
 | Results | 
Stations Plugs Utilization Load Profiles |  | 
Residential Access, PUMS
Driving Behavior
Charging Behavior
3rd Party Data/Simulations (e.g. POLARIS, BEAM, HIVE)
 | Network Design | 
Hierarchical Clustering Utilization Data |  | 
Levelized Cost
of Charging
CEC/EAD, CARB/MSS
Charging
Demand

## Slide 106: Bottom Up EVI-Pro Driving / Charging Simulations
NREL | 4
Departure | Arrival | Destination
7:00 AM | 7:45 AM | Public
9:30 AM | 10:30 AM | Public
12:45 PM | 3:00 PM | Public
4:00 PM | 5:00 PM | Home
Sample Vehicle / Infra Assumptions:
250 mile BEV
DCFC = 50kW
L2 = 7.2kW
Sample Choice / Access Assumptions:
Charge every night, home dominant
Plug-in only if needed, even at home
No home-charging, reliant on public infrastructure
Driving, Charging Simulations
Charging demand
to satisfy travel
None None None
Home L2 Home L2 None
Travel Data Discovered, Simulated Charge Events
Driver A Driver B Driver C
None None Public DCFC
None Public L2 None
Public L2
Home L2
Public DCFC

## Slide 107: EVI-Pro Lite
NREL | 5
Objective: Make analytic capabilities of EVI-Pro model accessible to broad group of stakeholders for EVSE investment decisions.
Approach: Develop a simplified, web-based interface for EVI-Pro that gives users access to a limited number of critical input variables.
Significance & Impact
EVI-Pro “unlocks” an unlimited number of scenarios for planners to explore regarding EV charging infrastructure requirements.
Ability to rapidly develop scenarios and explore sensitivities will help users understand the key drivers for investment.
afdc.energy.gov/evi-pro-lite

## Slide 108: EVI-Pro Lite: Providing complex modeling to a broad audience
EVI-Pro Lite simplifies demand modeling, enabling partners to create tailored scenarios for state or city charging infrastructure.
Building Partnerships
What are partners doing with the EVI-Pro Lite?
FHWA has highlighted the tool during state convenings on
nominating electric alternative fuel corridors
Hawaiian Electric Company built a case for infrastructure investment for the public utilities commission
Broward County, Florida directs consultants to use the tool for electric vehicle infrastructure strategies
Tesla uses the tool in discussions with cities around public infrastructure investments
NYSERDA planned infrastructure investment and has developed an ongoing partnership with NREL
Measuring Success
Since its launch, 6,000 users have viewed 14,000 pages on the tool, spending almost 4 minutes per visit.
NREL | 108

## Slide 109: EVI-Pro Lite: Providing complex modeling to a broad audience
EVI-Pro Lite simplifies demand modeling, enabling partners to create tailored scenarios for state or city charging infrastructure.
“Municipal and regional governments typically do not have the resources to understand their charging infrastructure needs. Having a quick online tool that gives a ballpark estimate of charging needs is a deeply helpful service. I’ve witnessed first-hand the amazement when city level sustainability staff first use EVI-Pro Lite.”
-DOE 2019 Annual Merit Reviewer
NREL | 109

## Slide 110: US Electricity Demand Scenarios
NREL | 8
NREL Electrification Futures Study scenarios project great degree of transportation electrification, in line with several energy system transformation scenarios
EFS High scenario, 2050
Transportation share of electricity use increases from 0.2% in 2018 to 23% of electricity consumption in 2050.
1,424 TWh increase in transportation-related electricity consumption relative to the 2050 Reference scenario.
Source: https://www.nrel.gov/analysis/electrification-futures.html

## Slide 111: Broad use of EVI-Pro for grid impacts analysis…

## Slide 112: “Unlock” EVI-Pro Load Profiles
With support from…
The US Department of Energy
In collaboration with…
Lawrence Berkeley National Laboratory
Schatz Energy Research Center at Humboldt State University
With feedback from…
Electric utilities Automotive manufacturers
Charging network companies
Local governments
Research institutes
Expose users to projections in:
A Simplified Interface for Accessibility A Programmatic Interface for Analysts

## Slide 113: “Unlock” EVI-Pro Load Profiles
Simulated load from 300,000 EVs in Massachusetts
PHEV40
BEV200
Emphasize significance of…
Vehicle Technology

## Slide 114: “Unlock” EVI-Pro Load Profiles
Home-Dominant Charging
No Home Charging
Emphasize significance of…
Residential Access
Simulated load from 120,000 EVs in Atlanta, GA
NREL | 12

## Slide 115: “Unlock” EVI-Pro Load Profiles
Home-Dominant Charging
Free Workplace Charging
Emphasize significance of…
Charging Behavior
Simulated load from 4,000 EVs in Denver, CO
NREL | 13

## Slide 116: “Unlock” EVI-Pro Load Profiles
Emphasize significance of…
Load Flexibility
Charge as soon as possible
Charge as late as possible
Simulated load from 2M EVs in Los Angeles
NREL | 14

## Slide 117: Demo of the Tool and API
afdc.energy.gov/evi-pro-lite/load-profile
developer.nrel.gov/docs/transportation/evi-pro-lite-v1

## Slide 118: EVI-Pro Lite – Load Profile
https://developer.nrel.gov/docs/transportation/evi-pro-
lite-v1/
https://afdc.energy.gov/evi-pro-lite/load-profile

## Slide 119: Initial form
Users select state and city/urban area on initial screen
May choose a larger fleet size, but max fleet size is restricted to 100% of current
light duty fleet

## Slide 120: Results page
Results show user inputs plus other default values
All values may be edited
Question mark icon on results page indicates more information is available

## Slide 121: Results page
Tooltips add context and clarification

## Slide 122: Results page
Load profile charts are greyed out and Recalculate button appears any time changes are made to inputs
Load profile shapes adjust once the Recalculate button is clicked

## Slide 123: Multiple scenarios allowed
Users can add or remove up to 5 comparison scenarios
Pre-defined “Best” and “Worst” case scenarios cannot be edited,
show minimum and maximum peak scenarios

## Slide 124: Multiple scenarios
When multiple scenarios are selected, charts change to a single line per scenario
Hovering over chart shows time of day

## Slide 125: Chart and input downloads
Two downloads available:
  Chart images (PNG, JPEG,
PDF, or SVG)
  Scenario inputs (CSV)

## Slide 126: Load Flexibility
Default scenario for EVI-Pro Lite is “minimum delay” – charging begins at full power/speed as soon as a user arrives at home or work and lasts until the vehicle is fully charged or unplugged
Inputs to represent load flexibility were added to the results page to demonstrate potential shifts in charging loads
Tooltip defines charging
strategies

## Slide 127: API and Methodology
Assumptions and Methodology content provided from page footer (https://afdc.energy.gov/evi-pro-lite/load- profile/assumptions)
API documentation for underlying APIs also linked from page footer (https://developer.nrel.gov/docs/transportation/evi- pro-lite-v1/)

## Slide 128
www.nrel.gov
Q&A
Eric Wood
eric.wood@nrel.gov

## Slide 129: What’s next?
What additional resources or effort is of most interest to you or your organization?
What additional data or functionality would be most useful for our residential end use load shapes?
What additional data or functionality would be most useful for our commercial end use load shapes?
What additional model functionality would be useful?
What topics do you hope we will cover in our final two TAG meetings?